## Slide 1
Nightlights along the Eastern Alpine river network in Austria and Italy
as a proxy of human presence
S. Ceola1, A. Montanari1,*, J. Parajka2, A. Viglione2, G. Blöschl2,3
1Dipartimento di Ingegneria Civile, Chimica, Ambientale e dei Materiali, Università di Bologna, Bologna, Italy
2Institute of Hydraulic Engineering and Water Resources Management, Vienna University of Technology, Vienna, Austria
3Centre for Water Resource Systems, Vienna University of Technology, Vienna, Austria
*e-mail: alberto.montanari@unibo.it
EGU Vienna – April, 18 2016 – SESSION HS2.3.3
Innovative sensing techniques and data analysis approaches to increase (eco)hydrological process understanding

## Slide 2
Overview & Motivation
Understanding the spatial and temporal distribution of human settlements and economic activities in relation to the geographical location of streams and rivers is of fundamental concern for several hydrologic issues (i.e., flood risk and drought management, water pollution and exploitation, stream ecological purposes).
This research study analyses the spatial and temporal evolution of human settlements and associated economic activity, derived from nighttime lights, in the Eastern Alpine region.
This study is a collaborative experiment performed in the context of the SWITCH-ON project between partners from University of Bologna and TU Wien. More information about the analysis and project are available at: http://www.water-switch-on.eu/.
EGU General Assembly – Vienna, 17th-22nd April 2016
SWITCH-ON is an EU FP7 Collaborative project (grant agreement No. 603587) under the Environment programme running from November 2013-October 2017

## Slide 3
Materials & Methods
River Network
Study Region Administrative Boundaries
EGU General Assembly – Vienna, 17th-22nd April 2016
SWITCH-ON is an EU FP7 Collaborative project (grant agreement No. 603587) under the Environment programme running from November 2013-October 2017
Satellite Nighttime Lights
Data Sets
River network: http://ccm.jrc.ec.europa.eu/php/
index.php?action=view&id=23
Austria: http://www.naturalearthdata.com/downloads/
10m-cultural-vectors/10m-admin-0-countries/
Veneto, Trentino Alto Adige and Friuli Venezia Giulia: http://www.istat.it/it/archivio/24613
Satellite nighttime lights: http://ngdc.noaa.gov/eog/dmsp/
downloadV4composites.html

## Slide 4
Materials & Methods
EGU General Assembly – Vienna, 17th-22nd April 2016
SWITCH-ON is an EU FP7 Collaborative project (grant agreement No. 603587) under the Environment programme running from November 2013-October 2017
Satellite Nighttime Lights
Time series from 1992 to 2013 (yearly average values)
Light is expressed through a Digital Number (DN) ranging from 0 (no light) to 63 (maximum luminosity), proportional to radiance
Spatial resolution: 30 arc second (0.00833°) – nearly 1 km at the equator
Spatial extension: 75° N – 65° S, 180° W-E
Nightlights as a proxy of anthropogenic presence
Human settlements and development in space and time

## Slide 5
Materials & Methods
EGU General Assembly – Vienna, 17th-22nd April 2016
SWITCH-ON is an EU FP7 Collaborative project (grant agreement No. 603587) under the Environment programme running from November 2013-October 2017
River Network
JRC’s Catchment Characterisation and Modelling (CCM, version 2.1) open database.
CCM2 is based on a pan-European DEM mosaic, updated land cover and climate data, and improved algorithms for data analysis.
Spatial resolution: 3 arc second
Spatial extension: entire European continent

## Slide 6
Materials & Methods
EGU General Assembly – Vienna, 17th-22nd April 2016
SWITCH-ON is an EU FP7 Collaborative project (grant agreement No. 603587) under the Environment programme running from November 2013-October 2017
Nightlights
River network
Intercalibration
Average of simultaneous satellites
Removal of gas flares
Intercalibrated nightlights
Identification of distance classes from river network
Study regions
Intercalibrated nightlight time series from 1992 to 2013 for Austria and N-E Italian regions
Intercalibrated nightlight time series from 1992 to 2013 at different distance classes for Austria and N-E Italian regions
River pixel
1 pixel from the river (~ 1 km)
2 pixel from the river (~ 2 km)
3 pixel from the river (~ 3 km)
4 pixel from the river (~ 4 km)
Frequency distribution analysis & Identification of statistics

## Slide 7
Materials & Methods
EGU General Assembly – Vienna, 17th-22nd April 2016
SWITCH-ON is an EU FP7 Collaborative project (grant agreement No. 603587) under the Environment programme running from November 2013-October 2017
Nightlights
Intercalibration
Average of simultaneous satellites
Removal of gas flares
Intercalibrated nightlights
DN: intercalibrated nightlight values
DNobs: raw nightlight data
C0, C1, C2: empirical intercalibration coefficients

## Slide 8
Identification of distance classes from river network
River pixel
1 pixel from the river (~ 1 km)
2 pixel from the river (~ 2 km)
3 pixel from the river (~ 3 km)
4 pixel from the river (~ 4 km)
Materials & Methods
EGU General Assembly – Vienna, 17th-22nd April 2016
SWITCH-ON is an EU FP7 Collaborative project (grant agreement No. 603587) under the Environment programme running from November 2013-October 2017
Given that the nightlight and river network spatial resolutions are different, the performed analysis focuses on different groups of river pixels and associated distance-from-river classes:
CCM river pixels with Strahler order ≥ 1 (i.e. all original river pixels are considered)
CCM river pixels with Strahler order ≥ 2
CCM river pixels with Strahler order ≥ 3
CCM river pixels with Strahler order ≥ 4 (i.e. only major rivers are considered)

## Slide 9
For each study region x and for each year t:
Identification of nightlight values in correspondence of each of the 5 distance-from-river classes j (i.e., j=0,4) for each pixel i, DNi,j(x,t)
Analysis of empirical frequency distribution of DNi,j(x,t)
Estimation of distance-from-river class average nightlight values DNj(x,t)
Materials & Methods
EGU General Assembly – Vienna, 17th-22nd April 2016
SWITCH-ON is an EU FP7 Collaborative project (grant agreement No. 603587) under the Environment programme running from November 2013-October 2017
Frequency distribution analysis & Identification of statistics

## Slide 10
Results
EGU General Assembly – Vienna, 17th-22nd April 2016
SWITCH-ON is an EU FP7 Collaborative project (grant agreement No. 603587) under the Environment programme running from November 2013-October 2017
Human signatures across the European Eastern Alpine region from 2013 nightlight data: CCM river pixels with Strahler order a) ≥ 1, b) ≥ 2, c) ≥ 3, d) ≥ 4

## Slide 11
Results
EGU General Assembly – Vienna, 17th-22nd April 2016
SWITCH-ON is an EU FP7 Collaborative project (grant agreement No. 603587) under the Environment programme running from November 2013-October 2017
Spatial and temporal trend of yearly nightlight values in Austria and Trentino Alto Adige

## Slide 12
Results
EGU General Assembly – Vienna, 17th-22nd April 2016
SWITCH-ON is an EU FP7 Collaborative project (grant agreement No. 603587) under the Environment programme running from November 2013-October 2017
Spatial and temporal trend of yearly nightlight values in Veneto and Friuli Venezia Giulia

## Slide 13
Conclusions
EGU General Assembly – Vienna, 17th-22nd April 2016
SWITCH-ON is an EU FP7 Collaborative project (grant agreement No. 603587) under the Environment programme running from November 2013-October 2017
The spatially and temporally extensive analysis of human signatures from nightlights provide valuable insights into the evolution of human presence
An overall enhancement of human presence across the considered distance-from-river classes during the last 22 years is revealed, though presenting some differences among the study regions
30% increment for Austria
15% increment for Trentino Alto Adige
12% increment for Veneto and Friuli Venezia Giulia
The river network delineation is found to play a major role in the identification of nightlight trends