## Slide 1
Is the likelihood of getting a flood increased by higher than usual flows in the previous months?
Presentation given at AGU Fall Meeting 2015 Session H52A Advances in Hydrometeorological Extremes Forecasting: Estimation, Integrated Risk Analysis, and Applications
Alberto Montanari University of Bologna alberto.montanari@unibo.it www.albertomontanari.it
Cristina Aguilar
University of Granada, caguilar@ugr.es
María J. Polo
University of Cordoba, mjpolo@uco.es

## Slide 2
We observed in the Po River that several flood events were preceded by long lasting high flows. Therefore, we wondered whether extreme floods are induced by long term stress, rather than a short sequence of extreme rainfall.
Research questions
We observed in the Po River that several flood events were preceded by long lasting high flows. Therefore, we wondered whether extreme floods are induced by long term stress, rather than a short sequence of extreme rainfall.
Research questions:
How long a river remembers its past?
Higher than usual flows in the low flow season might anticipate extreme events in the next high flow season?
The flood frequency distribution can be conditioned on the flow of the previous months?
By Baldo051 (Own work) [CC BY-SA 3.0 (http://creativecommons.org/licenses/by-sa/3.0)], via Wikimedia Commons

## Slide 3
Case studies: (1) The Po River

## Slide 4
Case studies: (2) The Danube River
From Wikipedia

## Slide 5
Persistence in river flows: a rich literature
It is well known that river flows are affected by forms of persistence that are not fully understood yet. These are referred to as the “Hurst Phenomenon”, or the “Hurst Effect”.
For a review, see:
P.E. O’connell, D. Koutsoyiannis, H. F. Lins, Y. Markonis, A. Montanari & T. Cohn - The scientific legacy of Harold Edwin Hurst (1880–1978), Hydrological Sciences Journal, in press (http://www.tandfonline.com/doi/abs/10.1080/02626667.2015.1125998).
It is well known that river flows are affected by forms of persistence that are not fully understood yet. These are referred to as the “Hurst Phenomenon”, or the “Hurst Effect”.
For a review, see:
P.E. O’connell, D. Koutsoyiannis, H. F. Lins, Y. Markonis, A. Montanari & T. Cohn - The scientific legacy of Harold Edwin Hurst (1880–1978), Hydrological Sciences Journal, in press (http://www.tandfonline.com/doi/abs/10.1080/02626667.2015.1125998)
The Hurst Effect has been physically explained as an implication of the principle of maximum entropy (Koutsoyiannis (2011, 2014)).
In practice, the Hurst Effect implies the presence of long term cycles over a multitude of time scales. Therefore, it could explain what we observed in the Po River.

## Slide 6
Po River Flows: yearly series

## Slide 7
Long memory (or long term persistence) in rivers
The presence of long memory implies the possible occurrence of long term cycles and therefore the persistence of high and extreme flows.
Long memory can be quantified through the estimation of the Hurst exponent (H)
Autocorrelation function
Time lag
H  [0 1]
H > 0.5 (long memory)
Rescaled range (R/S), aggregated variance (AV), differenced variance (DV)

## Slide 8
Fitting a Multivariate Probability Distribution for
(Annual Peak Flow) & (Average Flow in the previous low flow season)
We obtain two time series with sample size n, where n is the number of years in the observation period:
Yearly mean flow in the pre-flood season
Yearly peak flow in the flood season
The algorithm is flexible, allowing the user to select the periods arbitrarily.

## Slide 9
Fitting a Multivariate Probability Distribution for
(Annual Peak Flow) & (Average Flow in the previous low flow season)
Yearly average flow in the pre-flood season Qm
Yearly Peak flow in the flood season Qp
Normal quantile transform (with statistical tests)
Normal quantile transform (with statistical tests)
Multivariate Gaussian Distribution between 2 canonical Gaussian random variables
Distribution parameters:
m(Qm) = 0
s(Qm) = 1
m(Qp) = 0
s(Qp) = 1
r(Qp,Qm) to estimate
Updating the flood frequency distribution after the observation of Qm
Once r(Qp,Qm) is estimated, for an arbitrary (observed) Qm, the probability distribution of Qp is Gaussian, with parameters:
m(Qp) = r(Qp,Qm) Qm
s(Qp) = (1- r2(Qp,Qm))0.5
Therefore, the probability distribution of the peak flow can be updated after observing the average low flow in the considered season.

## Slide 10
Application to the Po River
Flood season: October and November
Correlation coefficient in the Gaussian domain between Qp and Qm for varying low flow season in the abscissa

## Slide 11
Updating the flood frequency distribution after the observation of Qm – Po River
Assumption: Oct-Nov peak river flows modeled through the EV1 distribution (Gumbel distribution)
Comparison between the unconditioned flood frequency distribution and the updated distributions for:
Higher than usual Sept Qm (70% quantile)
Higher than usual Sept Qm (80% quantile)
Higher than usual Sept Qm (95% quantile)
Distributions were fit on simulated data from the bivariate Gaussian distribution F(Qm,Qp), untrasformed from the Gaussian to the original domain through the NQT-1

## Slide 12
Updating the flood frequency distribution after the observation of Qm – Po River
Assumption: Oct-Nov peak river flows modeled through the EV1 distribution (Gumbel distribution)
Comparison between the unconditioned expected flood for return period of 200 years and the updated estimates for:
Higher than usual Sept Qm (70% quantile)
Higher than usual Sept Qm (80% quantile)
Higher than usual Sept Qm (95% quantile)
Distributions were fit on simulated data from the bivariate Gaussian distribution F(Qm,Qp), untrasformed from the Gaussian to the original domain through the NQT-1
Qm = average
Qm = 70% quantile
Qm = 80% quantile
Qm = 95% quantile
Qp = 12507 m3/s
Qp = 13023 m3/s
Qp = 13222 m3/s
Qp = 13790 m3/s

## Slide 13
Results for the Danube River
The results for the Danube are similar.
We assumed as flood season the period May-July.
The correlation is low with the river flow in March, which seems to be an anomaly.
We did not inspect yet whether negative correlation arise by moving further in the past seasons.
Correlation coefficient between peak river flow in the flood season and average flow in different pre-flood seasons

## Slide 14
In the context of the Switch-On Virtual Laboratory (www.water-switch-on.eu/), we would like to run with you a collaborative experiment. We would like to test our algorithm on other large catchments in the world.
We need:
a time series of average daily river flows, extended for at least 50 years.
Information on the catchment, including:
Please look at www.albertomontanari.it, where the experiment is presented and instructions are given.
The results will be presented in a publication that will be co-authored by the contributors.
Are you willing to make a collaborative experiment?

## Slide 15
Conclusions
The peak flow of the Po River and, to a lesser extent, the Danube River are sensitive to the average flow of the pre-flood season.
It is possible to update the probability of getting a flood, in a given year, 1-2 months in advance.
Looking for a physical explanation:
- Variability of the storage in the catchment;
- Variability in soil moisture conditions;
- Variability in the formation of net rainfall;
- Memory in the weather.
We need to check over more basins to gain nore insights, for an extended range of cacthment area and different climatic conditions.
There are open perspectives for extracting more information from the available data.

## Slide 16
Everything flows!
Thank you!