## Slide 1
Extreme values estimation under change: The never-ending dilemma (or sophism?) between Stationarity and Non-stationarity
Alberto Montanari
Department DICAM
Alma Mater Studiorum – University of Bologna
alberto.montanari@unibo.it
Two references:
Montanari, A: Hydrology of the Po River: Looking for Changing Patterns in River Discharge, HESS 2012
Montanari, A. and Koutsoyiannis, D.: A Blueprint for Process-Based Modeling of Uncertain Hydrological Systems, WRR 2012

## Slide 2
Sommary of the talk
Po River flood event occurred in 2000: the picture was personally taken at Polesine Parmense when the river stage peaked. Water reached the top of the levee which was protected with sandbags
What is flood change? Does the term “non-stationarity” describe flood change?
How can be flood change assessed and modeled?
The example of the Po River.
Conclusions

## Slide 3
What is flood change?
To assess flood change, let us refer to the continuous real variable “river flow” which we indicate with the symbol Q.
We have two alternative options to treat the variable Q:
1) Assume that Q is a deterministic variable
2) Assume that Q is a random variable
There is no other option.
Let’s choose option 1 (later on we will choose option 2), namely deterministic modeling. Then, to model Q we have to identify a deterministic relationship in the form:
Q = S(X,Q)
where X represent the input data and Q is the parameter vector of the model. X includes initial and boundary conditions and Q includes catchment behaviours like land-use etc. Note: both X and Q are deterministic variables (if they were random variables, then Q would be random as well). Note: In a deterministic model the outcomes are precisely determined through known relationships among states and events, without any room for random variation. A given input (including initial and boundary conditions) will always produce the same output and therefore uncertainty is not taken into account in a formal manner.

## Slide 4
Deterministic flood modeling
Q = S(X,Q)
The function S is governed by physical quantities and laws (gravity force, conservation of mass and energy, conservation of momentum, etc). Therefore, it is unlikely to undergo changes. Therefore changes in Q, if any, must be related to changes in X and Q. Given that X and Q are deterministic, the changes must be deterministic as well. This means that to model flood change one needs to deterministically describe changes in input data (mainly rainfall and temperature), initial and boundary conditions and model parameter vector (this latter including catchment characteristics, like land-use). Even if the function S cannot change, it is relevant to study its behaviours. In particular, it is significant to understand if it is upper bounded and, in general, to study how it responds to changes in X and Q. If it is upper bounded, it means that floods could be poorly sensitive to changes in input data and catchment behaviours. This is an issue that is frequently overlooked in climate impact studies.
Question? Is deterministic modeling feasible?

## Slide 5
In fact, Milly et al. (2008) refer to random variables in their well known Science paper.
A note on terminology
Please note: if we adopted deterministic flood modeling, the term “stationarity” and/or “non-stationarity” must not be used. In deterministic modeling they do not make any sense. What would the term “non-stationarity” mean for a deterministic variable? This latter is completely described by the deterministic function S (and the deterministic variables X and Q). We may wonder if the variable is upper or lower bounded, but the fact that it is a variable implies that it changes during time and therefore the “stationarity” concept does not make any sense. It is not just a matter of terminology. It’s a matter of concepts. We should forget the term “stationary” in deterministic environmental modeling.

## Slide 6
Stochastic flood modeling
Now, let us assume that Q is a random variable. Randomness can be treated by using many different approaches (fuzzy logic, possibility theory....). “The most comprehensive, elegant and complete way of dealing with uncertainty is provided by the theory of probability. In fact, probabilistic descriptions allow predictability (supported by deterministic laws) and unpredictability (given by randomness) to coexist in a unified theoretical framework…” (Montanari and Koutsoyiannis, 2012).
Let us using stochastics to model Q. Here the term “stochastics” s used to collectively represent probability, statistics and stochastic processes. Then, the relationship between Q and X and Q can be written as: f(Q)=K f(X,Q) where f is (joint) probability density function and K is a transfer operator that is related to the previously introduced deterministic relationship S. K can be random as well (Montanari and Koutsoyiannis, 2012).

## Slide 7
Stochastic flood modeling
f(Q)=K f(X,Q)
Changes in Q may occur after changes in the probability distribution of Q. These can be given by changes in K and/or changes in the probability distribution of X and Q. However, it is important to note that Q may change even if its probability distribution does not (think of long term cycles). Changes in probability distribution, if any, are related to non-stationarity. Within this context, the term is correctly used. In fact, stationarity is defined as (see Wikipedia): “...a stationary process (or strict(ly) stationary process or strong(ly) stationary process) is a stochastic process whose joint probability distribution does not change when shifted in time or space. Consequently, parameters such as the mean and variance, if they exist, also do not change over time or position”.
Therefore, in the stochastic view, detecting non-stationarity is indeed important for assessing flood changes.

## Slide 8
Stochastic flood modeling
f(Q)=K f(X,Q)
It is important to make clear what non-stationarity means.
Note 1: Definition of stationarity applies to a stochastic process
Note 2: Non-stationary processes have some of their statistical properties that are deterministic functions of time
(Koutsoyiannis, Hurst-Kolmogorov dynamics and uncertainty, Journal of the American Water Resources Association, 47 (3), 481–495, 2011).
Therefore, to detect flood change in the stochastic view one needs to identify a stochastic process describing floods, and detect whether the statistics of the process are a deterministic function of time. Note 3: non-stationarity applies to the stochastic process (the model) and not the real world. Nature has its unique trajectory, which is for sure changing along time.
Note 4: stationarity is an assumption that is introduced to simplify modeling of complex systems. In my opinion it is hardly dead.... For sure it has never been satisfied.

## Slide 9
Some first conclusions.....(1)
In the deterministic setting, detecting change means analysing deterministic changes in the deterministic inputs and deterministic parameters, and analysing the properties of the transformation S. In the stochastic setting, detecting change implies to identify a deterministic function explaining the changes along time of the statistics of the involved variables. To model change, we need to:
In the deterministic setting, reconstruct the form of the deterministic function S and describe deterministically the changes of X and Q along time.
In the stochastic setting, we need to build a stochastic model describing the detected changes of statistics in time. To do so, it is necessary to take full advantage of processes understanding through the transfer operator K
The real problem is change assessment. Once the information is available the model is not a significant problem.
On change assessment and modeling

## Slide 10
Some first conclusions.....(2)
Hydrological change is a very important issue today. Understanding change, its causes and effects, as well as adaptation strategies, is the challenge for the future.
Nature is for sure changing. There is no reason why it should be unchanging. The history of Nature provides plenty of examples of dramatic changes occurred in the past. Changes may occur for human impact and natural causes (remember: solar activity is the main driver and there is no reason for it not to change). Before embracing the deterministic or stochastic view, we should ask ourselves whether or not changes can occur randomly. This is a very important point. Changes can have positive effects. The history of humans is a continuous attempt to change Nature to create a more comfortable natural environment.
On hydrological change and changing Nature

## Slide 11
Some first conclusions.....(3)
Some examples of changing natural processes:
Glaciations (very far in time)
Medieval warm period (see http://en.wikipedia.org/wiki/Medieval_Warm_Period)
Example 1 from http://it.wikipedia.org/wiki/Matterhorn (in Italian): “The Italian name Cervino derives from the French "Cervin", which in turn derives from the Latin "Mons Silvanus", that is, woody mountain. Indeed, in the past centuries the climate over the region was warmer and favoured the growth of woods up to high altitudes. The warmer climate allowed people to cross alpine passes during most of the year. Such climatic "Optimus" was the reason of the importance of the Aosta Valley during Roman times and favoured the foundation of Augusta Prætoria Salassorum, the contemporary city of Aosta. Example 2 from http://it.wikipedia.org/wiki/Leggenda_della_valle_perduta (in Italian): “Walser people migrated beyond Monte Rosa during the 13th century, during the climatic optimum. The subsequent Little Ice Age prevented the alpine passes to be crossed and therefore the contacts with the original lands were lost. Therefore, the myth of a “lost valley” and a “lost city”, submerged by ice, was originated: the city of Felik, which is still witnessed by the toponyms of the Felik Glacier and the Felik Peak”. Note: from the climatic optimum to the Little Ice Age only 200 years passed. The change was very rapid! The current retreat of glaciers is likely to be occurring at slower pace than the previous advancement.
On hydrological change and changing Nature

## Slide 12
How can we detect change of statistics along time?
This is the key question – Remember: change must be deterministically explained. It is necessary to study the progress of statistics along time. This type of analysis, which is apparently easy, has been rarely done systematically (usually researchers focus on single series) for the following reasons:
Availability of computing means was limited till 20 years ago.
Data are scarce (but the situation is significantly improving).
Data are usually not shared – Difficult to implement a comprehensive analysis – People general limit the focus to case studies, which are hardly meaningful.
Data are uncertain – Need to put many data together.
It is problematic to estimate spatially averaged variables, like rainfall and temperature. Local changes can be cancelled out.
There are no codified statistical tests to detect non-stationarity – Need of a close interaction with statisticians.
Natural variables can be affected by local cycles. This fact is well proved but surprisingly it is often ignored (for political reasons).
There is still much to say on the detection of statistical tendencies! We need new tools!

## Slide 13
How can we detect change of statistics along time? Some hints for discussion
Refer to large areas – Do not limit the attention to single case studies or single countries. Look for collaborations.
Do not focus on river discharge only. Climatic variables are our drivers. It is a problem to obtain spatially averaged information. Focus on the estimation of spatially averaged values.
Do not limit the attention to extremes. We need to analyse all data!
Do consider uncertainty. It is not a limitation, but rather an intrinsic behaviour.
Do consider graphical techniques. A graphical representation is potentially able to tell us (and others) a lot of information.
Do consider the possible occurrence of local cycles (the Little Ice Age?). They are as important as permanent changes.

## Slide 14
The Po River is the longest water course that is entirely included in Italy
Main stream length: 652 km
Length of the natural stream network: about 7000 km
Basin area: 71.000 km2
Main tributaries: 141 (with min length of 20 km)
450 lakes – Regulation volume is about 1.3 km3
Precipitation volume: about 78 km3
Discharge volume at the sea: 60% of precipitation
Max river flow at the closure: about10.300 m3/s
Average river flow at the closure: about 1470 m3/s
The Po River Basin. Source: Wikipedia
The Po River example
Montanari, A.: Hydrology of the Po River: Looking for Changing Patterns in River Discharge - HESSD

## Slide 15
Temporal variability of river flows
Trends in annual maxima and minima – Pontelagoscuro 1920-2009
Regression line (with positive or negative slope) over a 50-year wide temporal window, starting from 1920

## Slide 16
3D visualisation of the complete Po River daily discharge series at Pontelagoscuro (1920-2009)
It is necessary to apply a filter to facilitate readability
Application of a moving average filter with width of 21 days along each year and 11 years along each day. A Gaussian filter is further applied with the same widths.
Temporal variability of river flows
Detailed analysis of the whole time series

## Slide 17
Detailed analysis if the whole time series 3D visualisation
Moving average and Gaussian filter
Temporal variability of river flows

## Slide 18
Conclusions
To assess and model hydrological change it is necessary to identify deterministic changes of the (statistics of the) involved variables.
To this end, refined techniques must be used to analyse the data, by considering the whole information that is available.
It is necessary to focus on extended data bases covering wide geographical regions. Let’s forget single case studies.
It is necessary to focus on the spatially averaged values of climatic variables.
Long term cycles are the real mistery. They are well known but not yet explained. They deserve particular attention.
Let’s embrace the stochastic representation to better understand hydrology. Deterministic representations prevent getting a complete picture of the underlying processes.
Good luck!

## Slide 19
Thank you!