## Slide 1
IAHS2017-382
Should we reconsider the conceptual structure of hydrological models?
Alberto Montanari Department DICAM – University of Bologna alberto.montanari@unibo.it – www.albertomontanari.it
This work has been partially funded by the research project PRIN 2015 -
“Mitigating the impacts of natural hazards on cultural heritage sites, structures and artefacts”, financed by Ministero dell’Istruzione, dell’Università e della Ricerca.

## Slide 2
Premise
Hydrology improved a lot in the past 30 years in terms of:
Computational means;
Monitoring capabilities;
Access to information;
Scientific communication.
However, the performances of hydrological models did not improve much and neither changed our approach to solve technical problems.
What is the reason why improved understanding and facilities did not lead into major technical advances?
Why is hydrology different with respect to sciences like meteorology and informatics that made major improvements?

## Slide 3
The scientific method in hydrology
We say and teach to our students that “Hydrology is the science of the movement, distribution, and quality of water on Earth and other planets”. We say that we have theories to explain hydrological phenomena.
We believe that science is driven by deduction through hypotheses.

## Slide 4
Are we missing something (1/3)?
We should be honest and recognize that in the past 30 years our theories did not progress much.
It would be interesting to discuss what major goals hydrology achieved in the past three decades. In my opinion we progressed in:
Model calibration and verification;
Uncertainty assessment (a little bit….);
Scenario analysis;
Process understanding (a little bit…. What do we know that Jim Dooge and Vit Klemeš – to cite only two eminent past hydrologists – didn’t?).
But what about theories and model performances?
What are we missing?
These considerations are inspired by a blog post by Carlo Rovelli, “Science Is Not About Certainty” (https://newrepublic.com/article/118655/theoretical-phyisicist-explains-why-science-not-about-certainty)

## Slide 5
Are we missing something (2/3)?
It may be that we are doing something wrong methodologically.
It may be that we need to change something in the conceptual structure that we use to understand hydrology. This would imply that we need to change the way in which we formulate hypotheses and construct theories from data.
To find inspiration, let’s refer to a significant example of a major discovery, namely, Einstein’s discovery of special relativity.
Einstein took very seriously Newtonian Mechanics and Maxwell’s equations for classical electromagnetism, but there were a contradiction between the two theories. The reason is that there was a universal, or absolute, notion of time.
By Gheorghe I. Manu - Gheorghe Jijie: George Manu – Monografie, Editura Elisavaros, Bucureşti, 2002, ISBN 973-8400-17-1, Public Domain, https://commons.wikimedia.org/w/index.php?curid=1330368

## Slide 6
Are we missing something (3/3)?
Einstein did not look for a new theory. He forced coherence between the two existing theories by challenging something completely different, which is how we think about time.
Einstein changed something in common sense – something about the elementary structure in terms of which we think of the world – and introduced special relativity, namely, one of the greatest discoveries of the XXth century.
How should we move forward then?
Past knowledge is an essential ingredient. Instead of assuming that it’s wrong or insufficient, we should wonder why it fails to provide a consistent picture of what we observe.
Science is not about certainty. Science is about finding the most reliable way of thinking at the present level of knowledge. In our conceptual structure for grasping reality, there might be something not appropriate, something we may have to revise.
Science is about continually going beyond common sense.

## Slide 7
How should we rethink the conceptual structure of hydrology?
By Ipipipourax - Own work, CC0, https://commons.wikimedia.org/w/index.php?curid=14758687
How did we deal with randomness so far?
To explain what we do not understand;
By admitting random behaviours for models’ components such as parameters;
By adding a random error to our models;
By ignoring randomness and assuming that a deterministic model provides a good estimate of expected values (which of course is a major flaw).
Perhaps we should admit that balance equations are successful but there is something wrong in the way we apply them.
Perhaps we should wonder why they fail.
Perhaps we should admit that we failed in recognizing the meaning and the role of randomness? (This is just my interpretation)

## Slide 8
How should we deal with randomness in the future?
By admitting randomness as a result of improved understanding (and not as a result of ignorance);
By admitting that our theories may fail if we do not account for randomness;
By formulating stochastic models, instead of plugging stochastic components into deterministic models;
By adapting our theories so that models provide a description of the probability distribution of outputs, rather than expected values plus uncertainty;
By looking for a physical basis to justify assumptions and randomness. We need to justify randomness through understanding (as opposed to lack of understanding).
By Nbeverly - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=35892827

## Slide 9
Going beyond common sense
Hydrology is driven by physical laws, but it is unquestionable that it involves randomness that will never be eliminated.
Therefore, the right way to follow may be a physically-based stochastic approach (rather than a deterministic model plus uncertainty). See Montanari and Koutsoyiannis (2012).
We should predict what can be predicted, by exploiting a process based approach, and task the stochastic model to provide uncertainty assessment for what cannot be predicted.
The goal should be to look for the conceptual approach that reduces uncertainty through process analysis (instead of trying to eliminate uncertainty).

## Slide 10
An example: the Shymod model project (1/2)
HyMod is a well known conceptual model that already includes a stochastic component. In fact, it represents contributing area to the surface runoff through a probability distribution. HyMod has been widely used, it counts 5 parameters.
Shymod stands for Stochastic HyMod.
The project aims to expand the stochastic structure of the HyMod model by allowing for stochastic parameters, stochastic catchment area, stochastic inputs. The project will also include a stochastic kernel into the model, which is a deviation from a single valued transformation, in order to account for uncertainty in model structure.
The project is under development in GitHub in the R environment.
A first version of Shymod is presented here where the catchment area is assumed to be a random variable.

## Slide 11
Why a stochastic catchment area (1)?
Catchment area is likely to change in different hydrological condition. When the catchment is unsaturated, there might be considerable infiltration and therefore flow paths do not follow the topographical surface. The actual catchment is not observable and therefore its area is random and likely dependent on degree of saturation.

## Slide 12
Why a stochastic catchment area (2)?
When the catchment is saturated, infiltration is negligible and flow paths follow the surface. It is an easier situation to model. In fact, we all know that flood modeling is relative easier than low flow modeling. In saturated conditions the catchment area is likely to converge to the value estimated from surface topography.

## Slide 13
Shymod assumption for catchment area
In Shymod the catchment area is a function of time according to the following relationship:
a(t) = a0 – c(t)/cmax (a0 – a)
where c(t) is catchment storage, whose upper value is cmax, a is the topographic catchment area, a0 is an outcomee from a calibrated random variable A0 that represent catchment area for c(t) = 0 and a is the catchment area estimated from the topographical surface.
Note that:
For c(t) = 0 (null catchment storage) then a(t) = a0
For c(t) = cmax (max catchment storage) then a(t) = a
Therefore catchment area converges to a for increasing catchment storage. Note that A0 is a random variable and therefore A(t) is a stochastic process.

## Slide 14
An example: the Shymod model project (2/2)

## Slide 15
Shymod application to 5 Italian catchments
Sieve@Fornacina:
a = 830 km2
3 years of hourly data
Arno@Subbiano:
a = 752 km2
22 years of daily data
Reno@Casalecchio:
a = 1061 km2
5 years of hourly data
Tanaro@Piantorre:
a = 521 km2
18 years of daily data
Gadera@San Lorenzo:
a = 394 km2
20 years of daily data

## Slide 16
Calibrating A0 on the whole record
Catchment area increases for increasing storage for all catchments but Gadera.
If the topographic catchment area is calibrated we notice slight overestimation for Sieve, Arno, and Reno, significant overestimation for Tanaro and underestimation for Gadera.
Nash efficiency improves 5-10% with the additional parameter. A0

## Slide 17
Conclusions
Let us look for new concepts: we do not necessarily need to predict everything. Let us recognize unpredictability. Let’s go beyond common sense!
Let’s appreciate the role and the physical justification of randomness. It is not an addendum, it is an intrinsic property.
Accounting for randomness is today possible: the Shymod project is a developing framework for applying a stochastic physically-based rainfall-runoff model.
Specifically, treating the catchment area, besides the contributing area, as a random variable allows one to highlight the dynamic structure and behaviour of catchments.
Randomness in hydrology is not about throwing a dice: it requires physically-based prediction of probabilities rather than trajectories.
This work has been partially funded by the research project PRIN 2015 -
“Mitigating the impacts of natural hazards on cultural heritage sites, structures and artefacts”, financed by Ministero dell’Istruzione, dell’Università e della Ricerca.

## Slide 18
Everything flows!
Thank you!