## Slide 1
EGU2016-13137
Sustainable co-evolution of society, ecology and hydrology: forward-looking modelling and prediction of the ecosystem and hydrology of the Lake of Monate – Italy
Session HS5.4
Advances in socio-hydrology
Alberto Montanari
Attilio Castellarin
Federico Cervi Department DICAM University of Bologna alberto.montanari@unibo.it www.albertomontanari.it

## Slide 2
The Lake of Monate is located in Northern Italy. It is a unique example of ecosystem that is close to pristine conditions, despite being located in a heavily urbanized area.
The Lake of Monate

## Slide 3
The reasons why the lake is in pristine conditions despite being located in a heavily human impacted area mainly three: one is purely hydrological while the other two are related to the societal asset:
The lake does not have surface tributaries. It is mainly fed by groundwater.
The lake coasts are mainly owned by private families, who are interested in keeping the lake clean and quiet. Therefore the public access is not possible, with the exception of a very small fraction of the shoreline (although the Italian law states that public waters and their shorelines are owned by the State)
The local administrators are committed to protecting the lake as part of their culture and history.
Note: the mountains surrounding the lake are subjected to mining activities since Roman times.
The Lake of Monate

## Slide 4
Lake of Monate
Lake Maggiore
Lake of Comabbio
Lake of Varese
The Lake of Monate has a glacial origin.
The only emissary is the Torrente Acquanegra.
The altitude of the water lever is about 266 m a.s.l.
The lake surface is about 2,6 km2.
The Lake of Monate: physical behaviours

## Slide 5
The Lake of Monate: physical behaviours
Lake of Monate
Mining site “Cava Faraona”
Mining site “Cava Santa Marta”
Lake of Comabbio

## Slide 6
The actual contributing area is greater than the topographic contributing area:.
The Lake of Monate: a distinguishing feature
The mining activities, which take place outside the topographic catchment and were recently re-activated, actually divert to another lake part of the rainwater originally contributing to the Lake of Monate. Furthermore, there is the concern that mining activities may interrupt preferential and significant flow. A spring that was supplying fresh water to the town of Travedona Monate up to the eighties of the past century suddenly ceased to deliver.

## Slide 7
Contributing area

## Slide 8
Are mining activities significantly impacting the hydrology and ecology of the Lake of Monate?
Is the hydrologic contribution of the mining site to the Lake of Monate significant?
Are mining activities impacting groundwater quantity and quality?
Plus:
Are vibrations induced by mining activities compromising the stability of hillslopes and buildings?
Is air quality affected by mining activities?
Take into account that mining activities provide a relevant societal benefit.
An interesting example of two ways interaction between societal and environmental systems.
Research questions

## Slide 9
Monitoring campaign
Monitoring of:
Hourly rainfall and temperature.
Hourly lake levels.
Daily river discharges.
Isotope composition in
groundwater.
Vibrations induced by
Mining activities.
Air quality.
Since September 2014.

## Slide 10
HyMOD (Boyle, 2000) was used for its flexibility.
5 parameters: Cmax, α, β, Kquick, Kslow
Human impact and feedbacks modelled by applying HyMOD to the catchment of the Lake of Monate and the catchment of the mining site, originally draining towards the Lake of Monate and now draining to the Lake of Ternate
Hydrological modelling and estimation of human impact

## Slide 11
Socio-hydrological modelling scheme
Two different calibration strategies:
Maximisation of the Nash-Sutcliffe efficiency for lake levels
Maximimisation of the above efficiency multiplied by the correlation between simulated groundwater flows and the average water table level in 2 piezometers

## Slide 12
Calibration and validation

## Slide 13
Validation

## Slide 14
Simulation over the whole observation period

## Slide 15
The best model seems to be the simpler one, which is the more robust. The best calibration strategy is the multiobjective solution, which takes into account the goodness of the fit of both the lake and the water table level.
The societal impact on the hydrological system is the major issue that this analysis considers. It is highly significant, not only for the impact of the mining activities on the lake ecosystem (which was adequately considered), but also for air quality, noise and vibrations (effects on the houses).
For the purpose of the present analysis, the impact of hydrological variables on societal benefit was neglected as the local community is only interested to preserving the lake ecosystem at the present stage. Moreover, such links are governed by the administrative procedures which are set up by the law in force which cannot be easily deciphered in mathematical terms.
Conclusions

## Slide 16
Socio-hydrological models should not be unnecessarily complex as complexity may make the model not representative.
If the hydrology-society link was considered by the model, social variables would need to be considered in calibration and validation. Representativeness of socio-hydrological models is a relevant issue for their use in transparent decision making.
Conclusions
This work is partially funded by the European Commission FP7 funded research project “Sharing Water-related Information to Tackle Changes in the Hydrosphere for Operational Needs” (grant agreement number 603587)