## Slide 1
EGU2016-3448
Is climate change modifying precipitation extremes?
Alberto Montanari(1) Simon Michael Papalexiou(2)
(1) Department DICAM - University of Bologna alberto.montanari@unibo.it www.albertomontanari.it
(2) Department of Water Resources and Environmental Engineering,. National Technical University of Athens
Session HS5.4
Advances in socio-hydrology

## Slide 2
Recent flood events in Italy – Sardinia 2013 and Genoa 2014

## Slide 3
Spatial distribution of natural catastrophes from 1980 to 2012
Source: MunichRE, NatCatSERVICE
Floods are the first cause of fatalities and economic losses among natural disasters worldwide
Emergency Events Database – EM-DAT, 2013

## Slide 4
Floods are the first cause of fatalities and economic losses among natural disasters worldwide
Temporal evolution of natural catastrophes from 1980 to 2012
Source: MunichRE, NatCatSERVICE
Emergency Events Database – EM-DAT, 2013

## Slide 5
Source: EARTH AT NIGHT 2012, https://earthdata.nasa.gov/labs/worldview
Nighttime lights are associated with the geographical position of the river network to locate the areas subjected to human pressure on water bodies

## Slide 6
The analysis shows a general increment of yearly-averaged nighttime lights from 1992 to 2012, thus revealing an increased exposure of human settlements to flood events during the last years
Results from Goal 1

## Slide 7
What about extreme precipitation? The situation in the US
Walsh, J., D. Wuebbles, K. Hayhoe, J. Kossin, K. Kunkel, G. Stephens, P. Thorne, R. Vose, M. Wehner, J. Willis, D. Anderson, S. Doney, R. Feely, P. Hennon, V. Kharin, T. Knutson, F. Landerer, T. Lenton, J. Kennedy, and R. Somerville, 2014: Ch. 2: Our Changing Climate. Climate Change Impacts in the United States: The Third National Climate Assessment , J. M. Melillo, Terese (T.C.) Richmond, and G. W. Yohe, Eds., U.S. Global Change Research Program, 19-67. doi:10.7930/J0KW5CXT.
Percent changes in the annual amount of precipitation falling in UN during very heavy events, defined as the heaviest 1% of all daily
events from 1901 to 2012 for each region. The far right bar is for 2001-2012.

## Slide 8
What about extreme precipitation? The situation in Europe
Consistent trends in mean annual precipitation have been observed, e.g. an upward trend in the North and a downward trend in
the South of Europe. However, for shorter time scales, the evidence is quite conflicting.
Data source: ENSEMBLES DATA provided by ENSEMBLE FP6 project - http://www.eea.europa.eu/data-and-maps/data/external/ensembles-data

## Slide 9
Data source: EURO-CORDEX data provided by EURO-CORDEX initiative: http://www.eea.europa.eu/data-and-maps/data/external/euro-cordex

## Slide 10
What about precipitation?
A global analysis of extreme rainfall is still lacking.
Rainfall data at fine time step are available in few locations only.
The purpose of this study is to carry out a global analysis of tendencies in rainfall extremes at global level,.
Criteria for selecting rainfall records
The database that was used in this study is the Global Historical Climatology Network-Daily database (version 2.60, www.ncdc.noaa.gov/oa/climate/ghcn-daily).
We initially selected the stations with record length greater than or equal to 5 years, with daily values assigned with quality flags less than 1% (see the above link for more details).
To further ensure data quality, among the several flags used, we deleted all values assigned with flags “G” (failed gap check) and “X” (failed bounds check).
These criteria resulted in a total of 68 014 stations located all over the globe.

## Slide 11
Global distribution of rainfall stations
Cells defined by latitude difference Δφ = 2.5° and longitude difference and Δλ = 5°

## Slide 12
Framework of the analysis
4 simple statistical analyses are carried out to detect changes in rainfall extremes along time:
Slope of extremes’ trend along time
Progress along time of yearly number of peaks over threshold
Progress along time of the number of peaks over threshold in 30-year long window
Trend along time in the number of maxima, their mean and standard deviation in 30-year long window
Thunderstorm in 1982.
From National Severe Storms Laboratory (NSSL) Collection, http://www.photolib.noaa.gov/htmls/nssl0050.htm

## Slide 13
1. Slope of extremes’ trend along time
For a daily precipitation record of N years we identify the N largest precipitation values (depicted with red dots in the left figure below). In the sequence, we fit a trend line and estimate its slope for every available 30-year period in moving 30-year framework (some fitted trends are shown in the left figure).
This analysis is performed for all available stations with at least 30 years of data, i.e., a total of 25,296 stations. Obviously, these records do not start the same year. The right figure depicts the number of stations having 30-year available period for every starting year after 1901.
We calculate the percentage of stations in all 30 year periods with positive slope.

## Slide 14
For the Northern emisphere (NH) starting after 1965 a rapid increase is observed in the percentage of stations with positive trends. It seems that there is an underlying sinusoidal pattern.
The same tendency can be seen at the global level.
For the Southern emisphere (SH) there is no clear tendency.
1. Slope of extremes’ trend along time - Results

## Slide 15
2. Progress along time of yearly number of peaks over threshold
In an N‑year daily record we identify the N maximum values and we count the number of them in each year.
This process is repeated for every available station and the sum of all maxima occurrences for each year and from all stations is calculated. The total number of considered stations varies from year to year.
Since we expect on average one maximum per year, then approximately for every i‑th year we should observe a number of maxima equal to the number of the considered stations.
We depict in a graph the percentage difference (PD) for every year between the observed number of maxima per year and the expected one.

## Slide 16
For the Northern emisphere (NH) a positive trend is observed in the number of maxima per each year
The same tendency can be seen at the global level.
For the Southern emisphere (SH) there is no clear tendency.
2. Progress along time of yearly number of peaks over threshold – Results

## Slide 17
3. Progress along time of the number of peaks over threshold in 30-year long window
We estimate the average number of extremes in all stations in moving 30-year periods, therefore obtaining for each station the time series ni where j denotes the starting year of the 30‑year period and n the number of extremes within the period. Under the assumption of stationarity this number should be equal to 30, given that we expect 1 value per year. This analysis is performed for all available stations and the average value of ni is estimated.
By Brocken Inaglory - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=2133657

## Slide 18
For the Northern emisphere (NH) a positive trend is observed in the number of maxima per each year
The same tendency can be seen at the global level.
For the Southern emisphere (SH) there is no clear tendency.
3. Progress along time of the number of peaks over threshold in 30-year long window – Results

## Slide 19
4. Trend along time in the number of maxima, their mean and standard deviation in 30-year long window
Selected statistics are computed for the daily rainfall data observed into a 30-yr moving window and a trend line is fitted to the progress of the statistics along time. If the slope is positive this means that more recent 30-yr periods have larger values of the given statistics, or even more generally, that the statistic of the process is increasing and thus the process is not stationary.
We would like to stress that this approach cannot lead to safe conclusions if applied to a single or just a few stations. A trend may just due to sample variability. Therefore, a trend is fitted to every available station and we calculate the percentage of stations having positive trends. If this percentage is large this is a strong indication of change.
We applied this method to a subset of the original stations, i.e., only to those stations having more than 50 years. We demand also records to have 30-years periods starting before 1940. The statistics studied are the number of maxima, the mean value and the standard deviation of the daily precipitation.

## Slide 20
For the Northern emisphere (NH) a positive trend is observed in the number of maxima per each year
The same tendency can be seen at the global level.
For the Southern emisphere (SH) there is no clear tendency.
For mean and standard deviation there is no clear tendency.
4. Trend along time in the number of maxima, their mean and standard deviation in 30-year long window – Results

## Slide 21
Conclusions
Although daily data are not representative of fine time scale phenomena, we observed a global increasing tendency in daily extremes in the recent past. It is more pronounced in the Northern emisphere.
Similar tendencies were observed in the past as well, but they were less pronounced, and finally reverted.
The overall analysis seems to confirm that both climate change and land-use change may have contributed to the recent increase in flood damages. The relative contribution of the two triggers may vary depending on local hydrology and local fluctuations in rainfall extremes. A careful assessment is needed to devise effective mitigation policies. We should not assume that climate change is the only driver. The interaction among drivers depends on the local context.
A more detailed analysis should focus on a limited region were finer time scale observations may be available.

## Slide 22
Acknowledgments
Simon Michael Papalexiou
National Technical University of Athens
This work is partially funded by the European Commission FP7 funded research project “Sharing Water-related Information to Tackle Changes in the Hydrosphere for Operational Needs” (grant agreement number 603587)

## Slide 23
Everything flows!
Thank you!