## Slide 1
Alma Mater Studiorum
University of Bologna
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it
To change or not to change,
that is the question
Alberto Montanari Professor of Hydrology – University of Bologna alberto.montanari@unibo.it - www.albertomontanari.it
Presentation delivered at the 2019 Dooge Medal Ceremony of IAHS
James C. Dooge (1922 –2010)

## Slide 2
Jim Dooge was a role model for his vision and comprehensive commitment in science for society. He experienced a multifaceted existence:
Engineer;
Scientist;
Academic;
Politician;
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it
Jim Dooge (1922-2010)
Irish Minister for Foreign Affairs;
Acting President of Ireland (Presidential Commission);
Chairman of the Irish Senate.
The story of Dooge’s Salmons
Jim Dooge designed the world’s first hydraulic fish lift. He understood that the main problem was to attract the salmons to the lock and realized they were attracted by white water. Therefore he designed the entrance of the lift to create turbulence.
The design had to be approved by fisheries inspectors. A small scale model was made as a test and 12 salmons were counted into the lower pool. The inspectors expected that all of them should make it to the top pool.
As the test began, at each lift run the inspectors counted the salmons that safely emerged at the top. Jim Dooge was reported to be quite nervous as the test went on.
At the end the inspectors counted 13 salmons – instead of 12 – at the top!
Dooge was very thankful to the 13th salmon!
Another demonstration that a deterministic setting may lead to a random outcome.

## Slide 3
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it
To change or not to change,
that is the question

## Slide 4
All of my research activity, since my master degree in 1992, was driven by the wish of studying
Change
M.Sc. thesis on water quality modelling under human pressure;
Ph. D. thesis on Hurst effect and long memory processes;
Stochastic models for river flow forecasting and water resources assessment;
Uncertainty assessment in hydrology (note: uncertainty is strictly related to change);
Land-use change impact assessment;
Climate change impact assessment;
Physically-based stochastic simulation for change assessment;
Non-stationary modelling;
Innovative information for change assessment;
Engineering of climate change adaptation.
From http://heavy-cloud-no-rain.wikia.com/wiki/The_Global_Hydrologic_Cycle?file=WaterCycleChanges.jpg12
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it
My research activity….

## Slide 5
IAHS initiatives: PUB, Panta Rhei and Unsolved Problems in Hydrology

## Slide 6
Panta Rhei: Community makes a difference

## Slide 7
A theoretical blueprint Physically-Based Stochastic (PBS) Modelling
Hydrological model in a deterministic framework:
Qp = S (Q, X)
Qp model prediction;
S model structure
X input data vector
Q parameter vector.
Hydrological model in a stochastic framework:
fQp (Qp) = K f Q, X(Q, X)
where f indicates the probability density function, and K is a transfer
operator that depends on model S.
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it

## Slide 8
Colors of uncertainty in stationary and non-stationary worlds

## Slide 9
A premise on stochastic models
“Stochastic” is a term that is very often used to mean the lack of a causal relationship between input and output, by often implying “lack of understanding”.
Deterministic model
Stochastic model
Impossible for lack of understanding?
Understanding the dynamics of the process
Is the process affected by uncertainty?
Stochastic model
(Expressing the dynamics in terms of probability)
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it

## Slide 10
The Galton Board
A demonstration that perfectly known systems may be impossible to predict deterministically but may be well predictable in stochastic terms.
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it
By Matemateca (IME USP), CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=59268653
Extracted from https://www.youtube.com/watch?v=4xViPStT5II&t=327s

## Slide 11
Attempts to explain randomness through deterministic relationships lead to misintepretation, overfitting, and eventually mistaken predictions
“The good researcher has the capability to dream by keeping the feet on the ground”
Ensemble predictions by deterministic models may not provide a consistent estimate of prediction uncertainty.
A sketch derived from a case study:
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it

## Slide 12
The fascinating question on Stationarity
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it

## Slide 13
Yet, another talk on climate change!
Images from:
Baluchi5 - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=22913585
Luis Prado, from The Noun Project [CC BY 3.0
(https://creativecommons.org/licenses/by/3.0)]
Jackl - Jackl, CC BY-SA 3.0,
https://commons.wikimedia.org/w/index.php?curid=2941245
Vincshekhan - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=8489443
Frits Ahlefeldt - HikingArtist.com - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=17001595
Bert Kaufmann from Roermond, Netherlands - Drought, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=24300268
By Wikilakz - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=62255747

## Slide 14
CC orders of magnitude – Temperature
(https://www.albertomontanari.it/?q=climatechange)
Global mean surface-temperature change from 1880 to 2017, relative to the 1951–1980 mean. The 1951–1980 mean is 14.19 °C (57.54 °F). The black line is the global annual mean, and the red line is the five-year local regression line. The blue uncertainty bars show a 95% confidence interval. By NASA Goddard Institute for Space Studies (http://data.giss.nasa.gov/gistemp/graphs/), Public Domain (https://commons.wikimedia.org/w/index.php?curid=24363898).
From: Koutsoyiannis, D. (2013). Hydrology and change. Hydrological Sciences Journal, 58(6), 1177-1197.

## Slide 15
CC orders of magnitude – Sea level
(https://www.albertomontanari.it/?q=climatechange)
Changes in sea level since the end of the last glacial episode. This figure was prepared by Robert A. Rohde from published data, and is incorporated into the Global Warming Art project. CC BY-SA 3.0 (https://commons.wikimedia.org/w/index.php?curid=479979).
Global mean sea level reconstructions over the period 1880-2012. Black line shows the three-year moving average. Red line shows data derived from satellite measurements. Data derived from 23 different gauges. By Robert A. Rohde, modified by A. Montanari - Image:Recent Sea Level Rise.png by Robert A. Rohde. This figure was prepared by Robert A. Rohde from published data, and is incorporated into the Global Warming Art project. Translation in french and conversion to svg was done by SuperManu, CC BY-SA 3.0 (https://commons.wikimedia.org/w/index.php?curid=3003623).

## Slide 16
The importance of variability
(https://www.albertomontanari.it/?q=climatechange)
Hydrologists have a unique knowledge of variability and change in environmental systems.
Long term cycles (Hurst effect) play a fundamental role in change, have implications in engineering design and climate change adaptation but they are often not considered. See my Wednesday’s presentation at https://www.albertomontanari.it/?q=node/215
Note: long term cycles may be human induced. They may be the effect of a positive feedback from the system to a human induced perturbation. They maybe the effect of resilience of the system.
Courtesy by Demetris Koutsoyiannis

## Slide 17
Goal of climate change adaptation
A graphic displaying the inter-connectivity between climate change, adaptability, vulnerability, and resilience..
Modified after Quokka-roo - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=32643177
Adaptation means anticipating the adverse effects of climate change and taking appropriate action to prevent or minimise the damage they can cause, or taking advantage of opportunities that may arise (from: https://ec.europa.eu/clima/policies/adaptation_en)
By Tommaso.sansone91 - Own work, CC0, https://commons.wikimedia.org/w/index.php?curid=77398870
From a technical (engineering) point of view we need to identify the relevant system and design variables.
Example: peak flow with assigned return period, water resources availability, environmental flow etc.
The key step is estimation of design variable(s) in the presence of uncertainty. This is common practice in engineering.

## Slide 18
Assessing climate impact – Traditional top-down approach
Future climate scenarios are generated through climate models;
Scenarios are routed through a simulation model to assess design variables;
System’s vulnerability are assessed and alternative strategies considered.
The top-down workflow is inadequate for technical design;
Climate models are not conceived to provide support to engineering;
The target of climate models is to depict “possible scenarios” (also called “projections”) according to given assumptions;
Their scenarios are precautionary. Their hypothetic use to support engineering design would lead to oversizing, with the possibility that solutions are impractical.
Uncertainty assessment for climate models does not take into account model structural uncertainty, and therefore the obtained confidence band is possibly biased.
Bias correction is not a solution.

## Slide 19
Decision theory – Bottom-up approach
(https://www.albertomontanari.it/?q=decisiontheory)
Decision theory has a long history of applications in water resources management;
Earlier techniques focused on optimisation and linear programming;
Multiple innovative techniques have been developed in the past 15 years, mainly in the context of climate change adaptation;
Information-Gap decision theory (Ben-Haim, 2001): defines a robustness function and a opportuneness function for each alternative. Shows the max range of uncertainty that can be tolerated.
Robust decision making (Bhave et al., 2016);
Assessing vulnerability in the presence of uncertainty
DECISION SCALING
Decision scaling (Brown et al., 2012):
  first evaluates the vulnerability of the considered system;
  Future scenarios are used to assess plausibility of vulnerability;
  Further information is used to estimate likelihood of vulnerability;
  Strategies are elaborated and selected.

## Slide 20
Types of solutions and their technical assessment
(https://www.albertomontanari.it/?q=decisiontheory)
Structural interventions;
Nature based solutions;
Plus other categories if one wishes….
By André Karwath aka Aka - Own work, CC BY-SA 2.5, https://commons.wikimedia.org/w/index.php?curid=2265672
A “magic” recipe does not exist. It is the “decision support system” that leads to the best combination of solutions.
Each alternative is to be assessed through:
Indicators (cost, disturbance to ecosystem, noise, any other relevant measure of performance);
Utility functions, translating the utility of each solution in terms of each indicator;
Overall utility of a solutions is computed through a weighted average of the utility associated to each indicator;
Pairwise comparison to assess weights (Saaty, 2008).
By Lou Sander - Own work I created this image from scratch., Public Domain, https://commons.wikimedia.org/w/index.php?curid=11154345

## Slide 21
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it
Geologic Clock
By Woudloper - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=2699855
To change or not to change,
that is the question

## Slide 22
An attempt to conclude
It is clear that we need to take change into account but….. Do we know change?
We have a good factual knowledge of change; We know that change is happening.
We still do not have full conceptual knowledge of change – We need to admit this. We still do not know change dynamics. We made little progresses recently.
We have a good procedural knowledge – We have models and methods, conditioned on conceptual assumptions. We recently made good progresses.
We still do not have a good metacognitive knowledge – We still do not have a clear idea of the optimal strategy to cope with change. We made good progresses recently but we still have a long way to go.

## Slide 23
An attempt to conclude
About conceptual knowledge: Full conceptual knowledge may still imply the presence of uncertainty.
About conceptual knowledge: human behaviour is subjected to uncertainty.
About metacognitive knowledge: should socio-hydrology rely on stochastic quantities, variables and parameters?
“A scientific method of inquiry must be based on observable and measurable evidence subject to specific principles of reasoning and experimentation.”
“For engineering design, we need robustness. Stationarity and linearity are immortal.”
Two concluding statements

## Slide 24
Thanks to my several mentors and collegues

## Slide 25
The most influencing mentors: Scientific Societies and their Members
Scientific societies turned out to be an immense source of inspiration and friendship
Thanks to the Dooge Medal Committee

## Slide 26
My great colleagues at Unibo!
Attilio Castellarin
Elena Toth
Serena Ceola
Alessio Domeneghetti
Alessio Pugliese
Cristiana Bragalli
...and also Marco Maglionico, Simone Persiano, Iuliia Shustikova, Mattia Neri, Francesca Carisi, Giada Molari!
Ph.D. Students and Post-Docs:
Paolo Leoni (2016-2018)
Serena Ceola (2012-2014)
Laura Lombardi (2008-2011)
Alessandro Bigi (2004-2007)
Laura Montanari (2002-2005)
Greta Moretti (2000-2003)
Elena Montosi (2009-2012)
Simone Castiglioni (2007-2010)
Giuliano Di Baldassarre (2003-2006)
Luigia Brandimarte (2002-2005)

## Slide 27
Science for the benefit of humanity? Let’s not to forget what’s happening just behind the corner.
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it