## Slide 1
Bluecat: A Local Uncertainty Estimator for Deterministic Simulations and Predictions (or: Understanding why a model is uncertain)
Demetris Koutsoyiannis
Alberto Montanari
Department of Civil, Chemical, Environmental and Material Engineering, Alma Mater Studiorum, University of Bologna
Presentation available at https://www.albertomontanari.it\\
Cropped from the picture available at https://www.flickr.com/photos/cizauskas/36142084534/ of the Andy Warhol exhibition at the High Museum, Atlanta, Georgia, USA (CC BY-NC-ND 4.0)
National Technical University of Athens, Zographou, Greece

## Slide 2
What is Bluecat?
We refer to a deterministic model transforming an input into an output
It can be a rainfall-runoff model, or any other deterministic model
Our purpose is:
To estimate uncertainty
To uncover the reasons for the presence of uncertainty

## Slide 3
How does Bluecat work?
A point prediction is obtained with a deterministic model.
A sample of neighbouring (in magnitude to the point prediction) simulated river flows is collected from the calibration period.
A corresponding sample of observed river flows is collected. This is used to estimate (from data) the probability distribution of the predictand conditioned on the point prediction.
The stochastic prediction is obtained along with uncertainty assessment.
Targeted selection of neighbours leads to identifying what is causing uncertainty.

## Slide 4
Bluecat theory (in brief)
Bluecat is given by the probability distribution of the predictand conditioned by the deterministically simulated river flow:
where q is true value and Q is the D-model prediction. They both refer at discrete time t.
A single deterministic model is considered, with a single parameter set. Extension to the multimodel case is straightforward.
The stochastic processes describing the modelled variables are stationary during the calibration and application period. This assumption can be easily removed.
Global uncertainty is resembled by the above conditional probability distribution, with no subdivision of uncertainty in different components. Bluecat automatically incorporates all types, including the uncertainty in input data and parameters, for which no particular provision is necessary.
The calibration data set is extended enough to ensure that sufficient information is available to upgrade the deterministic model (D-model) into the stochastic model (S-model).
Assumptions

## Slide 5
Bluecat application: determining the conditional distribution
We can use a parametric distribution like Pareto-Burr-Feller (Koutsoyiannis, 2021).
We can use a copula.
In Bluecat we propose a fully data based approach.
Data based approach
For each prediction by the D-model, we form a sample of size 2m+1 of neighbours in magnitude from the set of D-predicted data in calibration. The sample is centered around the D-model prediction.
We collect the corresponding observed data in calibration.
From the observed sample we pick the mean (or median) which gives the stochastic prediction, and the quantiles corresponding to the desired confidence level.
Beware: if, say, m=20, then the lowest and highest quantiles that can be empirically estimated would be 1/41=2.5% and 1-1/40=97.5%. Higher quantiles can be estimated by increasing m.
The above procedure is what we call “empirical estimation of quantiles through order statistics” for each prediction.

## Slide 6
Bluecat application: determining the conditional distribution
Robust empirical estimation of quantiles: K-moments approach
The above empirical estimation of quantiles through order statistics is based on one data point only, as it identifies the single observation that is closer in frequency to the probability that corresponds to the desired confidence level.
A possible solution to increase the robustness of the estimation is offered by the recently introduced concept of knowable moments (K-moments, see Koutsoyiannis (2019, 2021)) which gives an alternative for empirical quantile evaluation that is more reliable than order statistics as it combines many data points in each estimate.
This approach is not described here. Details can be found in Koutsoyiannis (2021, see picture on the right) and Koutsoyiannis and Montanari (2021).
The approach is applied in the Bluecat package (see below)
D. Koutsoyiannis, Stochastics of Hydroclimatic Extremes - A Cool Look at Risk, ISBN: 978-618-85370-0-2, 333 pages, Kallipos, Athens, 2021.
Free download at: http://www.itia.ntua.gr/en/getfile/2000/15/documents/StochasticsOfExtremes1.pdf

## Slide 7
Understanding uncertainty (or model diagnostic)
The “traditional” Bluecat regresses uncertainty against concurrent model simulation.
By selecting additional explanatory variables we can regress uncertainty against additional physically-based drivers.
In other words, we can understand why we fail in obtaining a “perfect” simulation (this is a provocative statement ).
Examples of additional explanatory variables:
- Season;
- Raising vs recessing limb;
- Catchment storage;
- Antecedent soil moisture.
Alternative hypotheses can be easily tested.

## Slide 8
The Bluecat Package
(https://github.com/albertomontanari/hymodbluecat)
R Environment, Bluecat associated to the HyMod rainfall-runoff model (Boyle, 2000).
Straightforward automatic calibration of HyMod.
User guide (very user friendly).
Step by step reproduction of the case studies presented in our paper.
Model simulation includes uncertainty assessment.
Easy and quick to install, runs on PC, try it!

## Slide 9
Bluecat application: Testing the goodness of the fit (included in the package)
Combined probability-probability plot (CPP): tests whether the marginal distribution of S-model predictions and true data are similar.
Predictive probability-probability plot (PPP): introduce by Laio and Tamea (2007) tests whether the conditional predictive distribution given by the S-model is providing a satisfactory interpretation of the corresponding conditional distribution of the true data.
Nash efficiency and correlation coefficient of S-model predictions (against D-model predictions).
Count of the percentage of points lying outside the confidence bands.
Modifified after Laio and Tamea (2007). Creative Commons License
Predictive probability-probability plot (PPP): introduce by Laio and Tamea (2007) tests whether the conditional predictive distribution given by the S-model is providing a satisfactory interpretation of the corresponding conditional distribution of the true data.

## Slide 10
Bluecat application: Arno River @ Subbiano case study
Catchment area: 752 km2
Daily river flow data predicted with HyMod.
Calibration period: 1992-2011
D-model Nash efficiency: 0.72
S-model Nash efficiency: 0.80
Percentage of data outside 80% bands: 10% (higher), 8% (lower)
Calibration

## Slide 11
Bluecat application: Arno River @ Subbiano case study
Catchment area: 752 km2
Daily river flow data predicted with Hymod.
Validation period: 2012-2013
D-model Nash efficiency: 0.66
S-model Nash efficiency: 0.70
Percentage of data outside 80% bands: 23% (higher), 20% (lower)
Validation

## Slide 12
Conclusions
In all of our applications the S-model provided improvements over the D-model.
The S-model includes the physical basis that is incorporated in the D-model. The improvement by the S-model is given by its capability to take randomness into account.
Bluecat is intuitive and transparent. It simply takes randomness into account by looking at model performances in the simulation of known data.
References are given in the papers available at the link below.
Presentation available at https://www.albertomontanari.it
Bluecat Homepage
https://www.albertomontanari.it/bluecat
Bluecat Papers
https://agupubs.onlinelibrary.wiley.com/doi/epdf/10.1029/2021WR031215
https://www.mdpi.com/2306-5338/9/5/86
Bluecat package (with HyMod Rainfall-Runoff model)
https://github.com/albertomontanari/hymodbluecat