## Slide 1
Alma Mater Studiorum
University of Bologna
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it
Long term cycles in hydroclimatic processes: the unresolved enigma of climatic variability
Alberto Montanari Professor of Hydrology – University of Bologna alberto.montanari@unibo.it - www.albertomontanari.it
“You must welcome change as the rule but not your ruler” (Denis Waitley)

## Slide 2
Why this talk
The so-called “natural variability” of climate is a topical issue. Can climatic and hydrological variables be characterised by “natural” ups and downs? We know the answer is yes, but what are the causes?
Variability of hydrological processes is related to the Hurst phenomenon / long term persistence (LTP) / long memory.
It’s a topic that was widely studied in hydrology. It is much relevant for climate change adaptation. Solutions to cope with variability are different with respect copying with trends. Design approaches are also different.
Example: sizing of reservoirs is affected by long term trends and variability.
From slides prepared by Bibhabasu Mohanty, Dept. of Civil Engineering, SALITER, Ahmedabad

## Slide 3
Variability 1/3 – River flow
(More details at: https://www.albertomontanari.it/?q=climatechange)
Montanari, A. (2012). Hydrology of the Po River: looking for changing patterns in river discharge. Hydrology and Earth System Sciences, 16(10), 3739-3747.
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it

## Slide 4
Variability 2/3 – River flow
(More details at: https://www.albertomontanari.it/?q=climatechange)
Montanari, A. (2012). Hydrology of the Po River: looking for changing patterns in river discharge. Hydrology and Earth System Sciences, 16(10), 3739-3747.

## Slide 5
Variability 3/3 (or trend?) – Extreme rainfall
(Papalexiou and Montanari – WRR 2019 - https://doi.org/10.1029/2018WR024067)
Mean trend values of frequency (events/decade)and magnitude (mm/decade)of extreme daily precipitation in large geographical zones over the period 1964-2013. Maps show the results for globe, North hemisphere, Northwest quadrant, Northeast quadrant, Southeast quadrant (zones are indicated by insets with global maps).
Mean trend values in 5°×5°grid cells in extreme daily precipitation over the
period 1964-2013. Maps show trends in frequency as number of extreme events per decade.

## Slide 6
Our current focus: Droughts in the Bologna region
Annual rainfall in Bologna (1813 – 2009)
Long term droughts occurring periodically;
Last one occurred during 1945 – 1950;
Guo and Montanari (2023)
Historical analysis of past droughts delivers more conservative drought risk prediction than 13 GCMs running up to 2100.
Droughts controlled by long term correlation.
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it

## Slide 7
Variability or trend? Beyond short term: Long Term Persistence
Long term persistence – also called long memory – gives rise to the Hurst Effect.
The Hurst effect was discovered by the English hydrologist Harold Edwin Hurst.
It is essentially due to the presence of long-term cycles, with different temporal scales, in the process.
It is one of the most studied topics in hydrology and water resources management. Curiously it is still poorly known and frequently ignored by the literature on climate change.
With Stephen Hurst, - Hurst’s son at a IAHS meeting in Kos (Greece), 2013
Random Gaussian process N(0,1)
Gaussian process N(0,1) with H=0.8
The intensity of long term persistence can be measured by the Hurst parameter H, with 0 ≤ H < 1. H ≤ 0.5 means absence of LTP.
LTP entails larger uncertainty and therefore has a significant effect on engineering design.
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it

## Slide 8
Estimating LTP (1/2)
Most methods for estimating H are heuristic approaches for assessing the fluctuations of the process. The intensity of LTP (the value of H) is related to the amplitude and duration of fluctuations around the mean of the process.
Note: it is well known there is uncertainty in LTP estimation. Bias can be induced by the presence of trend and seasonality. There is an extended literature on this matter.
Analysis of variance
From: Koutsoyiannis D., Generic and parsimonious stochastic modelling for hydrology and beyond, doi:10.1080/02626667.2015.1016950 https://www.researchgate.net/figure/a-Autocorrelogram-and-b-climacogram-of-a-time-series-of-100-terms-generated-from-the_fig5_281031174
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it

## Slide 9
Physical evidence: (linear) trend
Anthropogenic influence;
CO2 emissions;
Water cycle alteration (for instance, land-use change);
Hydraulic structures (dams, detention basins etc).
Physical evidence: LTP
There are plenty of possible explanations for long term cycles in hydrology and climate;
Orbital changes;
Extreme events (volcanic eruptions);
Catchments dynamics;
Superimposition of several autoregressive processes with random autocorrelation structure;
More and more still to discover….
Note: Koutsoyiannis (2011) proved that LTP arises from maximization of entropy in stochastic representations of natural processes.
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it

## Slide 10
River memory: a possible explanation for LTP
Iliopoulou et al. (2019) analysed a large sample of European river flows.
They found significant correlation of high flows/low flows with the mean flow of the previous month.
Drivers of correlation are catchment storage potential and other hydrological behaviours.
Correlation and LTP may be originated by other processes and variables than precipitation.
Many research questions are still open on the interaction between hydrology and climate.
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it

## Slide 11
Models for explaining tendencies – Engineering design
Linear trend (as well as other types of trend – polynomial, exponential and so forth) and LTP are alternative models to explain the tendencies that we may find in the data. Note: LTP originate a trend at local temporal scale.
Sometimes available data could not allow to discriminate between alternative models/alternative physical explanation.
Engineering design needs to consider flexible solutions that may efficiently cope with tendencies at different time scales. No-regret solutions may be an opportunity but we need to integrate solutions that are efficient at different time scales.
Decision theory has recently proposed advanced methods to cope with uncertain future scenarios. See, for instance, decision scaling (Brown et al., 2012).
DECISION SCALING
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it

## Slide 12
Solving the rebus – Take home message 1/2
Deciphering the role of variability – i.e., discriminating between irreversible tendency and local cycle – is extremely important for designing climate change adaptation strategies.
For most of the processes we deal with, the current knowledge and information (data) does not allow one to reject either models. Therefore we should not reject the hypothesis that local tendencies may be part of long term cycles.
Innovative physical knowledge and the availability of more and more (openly accessible) information allow us to move substantial steps forward.
Taking into account long-term persistence is particularly important when estimating drought risk and sizing reservoir as well as other measures to cope with droughts.
Diversification of interpretations and measures is the key to mitigate climate-related risks.
By Videoplasty.com, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=67135363
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it

## Slide 13
For generating future hydroclimatic scenarios models that can reproduce both the change in statistics and the long term persistence patterns should be used. This goal may be achieved by coupling stochastic LTP models with climate models.
Keep in mind the diversity of time scales. Integration of different strategies, and in particular integration of mitigation and adaptation, is needed to cope with tendencies at different time scales.
Bottom-up approach requires adaption strategies.
“Physically-Based-Stochastic (PBS) change simulation“
PBS Change Simulation
Solving the rebus – Take home message 2/2

## Slide 14
This presentation is available at the web address http://www.albertomontanari.it – E-mail: alberto.montanari@unibo.it
References
Brown, C., Ghile, Y., Laverty, M., & Li, K. (2012). Decision scaling: Linking bottom‐up vulnerability analysis with climate projections in the water sector. Water Resources Research, 48(9).
Koutsoyiannis, D. (2016). Generic and parsimonious stochastic modelling for hydrology and beyond. Hydrological Sciences Journal, 61(2), 225-244.
Koutsoyiannis, D. (2011). Hurst-Kolmogorov dynamics as a result of extremal entropy production. Physica A: Statistical Mechanics and its Applications, 390(8), 1424-1432.
Marani, M., & Zanetti, S. (2015). Long‐term oscillations in rainfall extremes in a 268 year daily time series. Water Resources Research, 51(1), 639-647.
Montanari, A. (2012). Hydrology of the Po River: looking for changing patterns in river discharge. Hydrology and Earth System Sciences, 16(10), 3739-3747.
Montanari, A., & Koutsoyiannis, D. (2012). A blueprint for process‐based modeling of uncertain hydrological systems. Water Resources Research, 48(9).
Montanari, A., Rosso, R., & Taqqu, M. S. (1997). Fractionally differenced ARIMA models applied to hydrologic time series: Identification, estimation, and simulation. Water resources research, 33(5), 1035-1044.
Papalexiou, S. M., & Montanari, A. (2019). Global and Regional Increase of Precipitation Extremes under Global Warming. Water Resources Research.