## Slide 1
Coastal Hydrodynamics and Morphodynamics

## Slide 2
Coastal hydrodynamics and morphodynamics
Coastal hydrodynamics and morphodynamics studies the circulation of sea water in the proximity of the shoreline, as well as the associated erosive process and sediment transport.
The above processes evolve along different spatial and temporal scales, according to complex dynamics that are driven by several forcings and impacted by several environmental behaviors. The latter include the wave and wind regimes, the geometry of the embayment, the presence of coastal protections, the shape and geology of the coast, the sediment size of the beach and many others.
The morphodynamic approach to beaches and coastal systems recognizes the range of interactions among the above processes occurring across the full environmental system.

## Slide 3
Coastal hydrodynamics and morphodynamics
Basic nomenclature of a sea wave. By NOAA - http://oceanservice.noaa.gov/education/kits/currents/media/supp_cur03a.html, Public Domain, https://commons.wikimedia.org/w/index.php?curid=50074693.

## Slide 4
Wave forcing
Coastal hydrodynamics and morphodynamics is driven by wave forcing.
The dynamics of wind waves is characterized by the presence of randomness, which determines their height, duration, and shape with limited predictability. The physics of waves is governed by the following main drivers:
1) Wind speed and duration. Wind is the sources of energy for wind waves and therefore regulates the energy transfer from wind to waves.
2) The uninterrupted distance of open water over which the wind blows without significant change in direction (called the fetch).
3) Width of area affected by fetch.
4) Sea depth.

## Slide 5
Wave forcing
In open sea and ocean, the movement of the waves is given by a shift of forms rather than mass of water. If fact, waves are the expression of a shift of energy rather than mass. Only after breaking a significant movement of mass of water occurs back and forth in the swash zone.
The size of a single transversal sea wave (namely, a wave that is oscillating perpendicularly to the direction of propagation) and its propagation is characterized by the following main behaviors:
1) Wave amplitude.
2) Wave length.
3) Wave period or frequency.
4) Wave direction.
In open ocean, it is convenient to refer to plane waves, namely, waves whose wavefronts (surfaces of constant phase) are infinite parallel planes.

## Slide 6
Along shore sediment transport
Breaking waves close to the shoreline combine with along shore currents to originate the transport of beach sediments.
Displacement of sediment may take place at the local level or may be extended over long distances in the along-shore and cross-shore directions.
Along-shore sediment transport is responsible of long term variations. Cross-shore erosion and deposition is responsible of rapid shocks during extreme events.
Sediment transport may occur in the form of bed-load and suspended transport.

## Slide 7
The CERC formula
In engineering applications, the longshore sediment transport may be expressed as the volume transport rate Ql. It may be expressed in cubic meters per day or year. It may also be given in immersed weight transport rate, which can be easily related to the volume transport rate once the mass density of the sediment grains and water are known.
Let us assume that the total longshore sediment transport rate is related to the longshore component of the energy flux which is generated by waves that approach the shore at an angle. We indicate with the symbol Eb the wave energy density per unit horizontal area at the breaker line.
Let us recall that the wave energy is given by the sum of the kinetic and potential energy density, integrated over the depth of the fluid layer. Potential and kinetic energy oscillate during the wave phase by compensating each other, so that the total energy is conserved (under ideal conditions) and is equal to the mean wave energy.

## Slide 8
The CERC formula
The potential mean energy density for a periodic wave can be computed through the relationship
It can be proved that according to the linear wave theory the mean kinetic energy density per unit horizontal area is equal to the above mean potential density per unit horizontal area. Therefore the total energy density of the wave at the breaker line per unit horizontal area is given by
Note that total energy is constant along the wave period (see Figure) and therefore we do not need to refer to any mean value.

## Slide 9
Potential and kinetic energy

## Slide 10
The CERC formula
The same result can be achieved by considering that the kinetic energy of the periodic single plane wave is null when the wave reaches the upper and lower elevation. Therefore the total energy at the breaker line is equal to the potential energy of the wave at the upper and lower elevation which is given by the relationship
As waves propagate, their energy is transported. The energy transport velocity is the group velocity. As a result, the wave energy flux, through a vertical plane of unit width perpendicular to the wave propagation direction, is equal to

## Slide 11
The CERC formula
Cbg is the wave group velocity at the breaker line. The latter can be estimated through the relationship
where k = Hb/db is the breaker index.
Then, we define the potential longshore sediment transport rate Pl as the immersed weight of sediments per unit time that may be potentially transported for given sea and shoreline conditions provided enough material is available to be transported. It may be estimated through the relationship

## Slide 12
The CERC formula
Here αb is the acute angle between the breaker line and the coast line. On the one hand, multiplication by sinα leads to obtaining the longshore component of the energy flow; on the other hand, multiplication by cosα allows one to account for the reduced wave breaking that occurs when waves approach the coast with a direction that is close to that of the shoreline. In the limiting and unlikely situation that wave direction is parallel to the shoreline wave breaking is negligible along with the transportation of sediments. If one assumes that the longshore transport is proportional to cosα then the most impacting situation occurs when α=45°.

## Slide 13
The CERC formula
With simple transformations of trigonometric functions Pl can be computed as
The immersed and "actual" weight transport rate can be obtained by multiplying Pl by an empirical coefficient, namely,
where K is a dimensionless parameter with 0 ≤ K ≤ 1. The above relationship can be converted to a volume transport rate:
where ρs, ρ and n are the mass density of sediment grains, mass density of water and sediment porosity, respectively. For several computations a value K = 0.7 is used.