## Slide 1
Salt water intrusion

## Slide 2
Salt water intrusion
Saltwater intrusion is the flow of seawater into fresh water water bodies like rivers or aquifers due to natural processes or human activities. It is a major concern for most coastal areas as it can induce contamination of water resources and therefore drinking water, and may cause damage to agriculture.
It is also a concern for the quality of coastal ecosystems as it may undermine the conditions of vegetation and therefore the stability of dunes, and may compromise coast wetlands, therefore impacting their ecosystem services, with implications in coastal socio-economy.

## Slide 3
Drivers of salt water intrusion

## Slide 4
Drivers of salt water intrusion

## Slide 5
Drivers of salt water intrusion

## Slide 6
Dynamics of salt water intrusion

## Slide 7
Darcy’s law
Groundwater flow takes place at the microscopic scale through movement of water particles along soil pores. As such, it is typically a 3-dimensional (3-D) flow. Stochastic models are thus typically used.
If we focus on the flow properties averaged over sufficiently spatial scale, the groundwater flow can generally be efficiently represented by using 1-dimensional (1-D) models, under the assumption that the velocity vector for each water particle does not change along two spatial directions. This assumption implies that the water flow is gradually varied, that is, that the stream lines are sensibly rectilinear and parallel. It follows that the distribution of pressure in each cross section follows the hydrostatic law.

## Slide 8
Darcy’s law
Under the above assumptions, groundwater flow takes place according to Darcy's law, which states that the volumetric flow rate for a 1-D water flow is a function of the flow area, potential energy, fluid pressure and a proportionality constant. The law was formulated by Henry Darcy based on the results of experiments on the flow of water through beds of sand. According to Figure 5, Darcy's law states that the total discharge, Q (units of volume per unit time) is equal to the product of the hydraulic conductivity of the medium, κ (units of velocity), the cross-sectional area to flow, A (units of area), and the gradient along space of the hydraulic head J (adimensional), namely:
Q = k A J = k A ∂H/∂x
where x is the flow curvilinear coordinate (note that flow is 1-D and therefore H varies along x only) and H is hydraulic head.

## Slide 9
Darcy’s law
Water flows in the direction of decreasing head and therefore the head itself determines whether the flow is directed towards inland or the sea. The hydraulic head represent the energy of flow for unit weight of water. Under the assumption of very limited velocity of the flow, the hydraulic head is the sum of elevation head and pressure head. Namely, for a given water flow a groundwater body, the hydraulic head of an arbitrary fluid particle in a given flow cross section is given by
H = z + p/γ
where z is the elevation of the fluid particle itself with respect to a reference level and γ is the specific weight of the fluid. The above mentioned hydrostatic law suggests that H is constant in each cross section of the water flow itself.

## Slide 10
Infiltration of salt water in coastal aquifers

## Slide 11
Infiltration of salt water in coastal aquifers
We assume that aquifer and sea are in steady state conditions and there is no mixing at the interface between salt water and fresh water. A simple application of hydrostatics leads to determining the position of the interface between salt water and freshwater. Saltwater has a higher content of dissolved salts and minerals and thus it is denser than freshwater therefore inducing a higher hydraulic head. An analytical relationship was independently proposed by Badon Ghijben and Herzberg, by taking into account that salt and freshwater have different densities, which reads as
H = α h
where H is the depth of the interface with respect to sea level along a given vertical and h is the height above sea level of the water table in the same vertical. α is given by ρf / (ρs - ρf)/ where ρs and ρf are the densities of salt and fresh water, respectively.

## Slide 12
Infiltration of salt water in coastal aquifers
If we assume that ρs=1025 kg/m3 and ρf=1000 kg/m3 then one obtains
H = 40 h .
Given that the height of the water table generally increases while moving inland, saltwater moves into coastal aquifers in a wedge shape under the freshwater. Ordinarily the inland extent of the saltwater wedge is limited because fresh groundwater levels, or the height of the freshwater column, increases as land elevation gets higher.

## Slide 13
Infiltration of salt water in coastal aquifers
The interface models given by the Badon Ghijben-Herzberg principle provides a coarse approximation of what actually happens in a coastal aquifer systems. In fact, the underlying assumptions are not met in practice and therefore some restrictions on the applicability of the principle should be considered:
First, the brackish zone between fresh and saline groundwater should only be schematised by an interface when the thickness of the brackish zone is very limited. This condition applies only in rare situations where the freshwater lens receives significant recharge.
Second, the principle assumes a hydrostatic equilibrium, whereas in reality the aquifer system might considerably deviate from this equilibrium situation. In those cases, e.g. in freshwater bodies near the shoreline, the Badon Ghijben-Herzberg principle should not be applied, because the computed position of the interface deviates from the actual position as the coast is approached.

## Slide 14
Drivers of salt water infiltration in coastal aquifers

## Slide 15
Infiltration of salt water in coastal aquifers
Factors that affect the saltwater - fresh water interface may be natural or human induced. They may be classified according to their spatial scale, ranging from global to regional and local.
Global scale factors include:
Rising of sea water level; it may be caused by land subsidence (relative sea level raise), ice cap melting after climate change and thermal expansion of sea water after global warming.
Change in precipitation: a slower infiltration rate into aquifer to replenish the amount of fresh water may induce a lowering of the water table.
Increased evapotranspiration: it may be due to global warming (but there is no consensus on the the effect of global warming on evapotransiration) or increased irrigation (in this case it is a local or regional factor).

## Slide 16
Infiltration of salt water in coastal aquifers
Regional scale factors include:
Subsidence: it may be due to oil and gas extraction, water pumping, or soil compaction.
Local climate change: it may be due to heat island effects or other local forcings.
Urbanisation: it reduces the recharge of aquifers.
Local scale factors include:
Change in soil permeability: due to the construction of barriers or soil compaction.
Increased Consumption of Water: increased water demands for civil and agricultural use.
Water pumping: it is a very frequent determinant of saltwater intrusion. Pumping lowers the level of the water table. Saltwater can contaminate freshwater resources by interfering with the wells therefore increasing the salinity of drinking water.

## Slide 17
Monitoring
Monitoring is essential to prevent and mitigate the impact of saltwater intrusion. It can be carried out by using direct and indirect methods. Direct methods include measurement of groundwater salinity profiles and groundwater sampling of observation and active wells. Direct methods were mostly used to detect groundwater salinity up to recent times. Indirect methods are mostly based upon geophysical techniques such as ground penetrating radar. The device produces a continuous cross-sectional picture of shallow subsurface conditions. Measurement of electrical conductivity is also widely used. Observations indicate the concentration of dissolved solids that are present as ions (charged molecules) in a polar solution like water. In a mix of seawater with freshwater for example, chloride is typically one of the predominant ions present, therefore electrical conductivity can be used as a relative measure of chloride concentration.

## Slide 18
Recovery
Synthesis of strategies, approaches, and tools to mitigate the impacts of saltwater intrusion in coastal regions (from White and Kaplan, 2017).