## Slide 1
Assessing water resources availability
Inductive methods

## Slide 2
Estimation of water resources availability is an essential step for devising efficient water resources management strategies (see the Wikipedia page for “water scarcity”.
Assessment of surface water resources is less complicated with respect to groundwater, for the observability of surface water bodies.
The most relevant challenge when assessing water resources is lack of data. This is a widespread problem in hydrology, as observations of climate and hydrology started relatively recently.
History of water resources systems (interactive learning).
Water Resources Availability

## Slide 3
Lakes are relatively easy to manage provided the recharge is quick. Lakes may be regulated.
Rivers are frequently dealt with, by assessing the dynamics of river flow.
Either “inductive” or “deductive” methods (or “direct” and “indirect”).
Reference is usually made to a cross river section, namely, the geometric figure that is obtained by cutting the river with a plane that is perpendicular to the velocity vector for a given fluid particle within a river flow (remember the definition of water flow).
Assessment of Water Resources Availability

## Slide 4
Reference to a location and corresponding cross section.
Water flow is the volume of water per unit time that passes through the cross section. In a river it is also called “discharge”.
Measuring water discharge for a long time allows one to assess water resources availability.
Estimation of flow duration curve – transparent and simple (FDC)
Inductive Assessment of Water Resources Availability

## Slide 5
The FDC depicts the percentage of time (duration) over a given observation period during which a given streamflow is equalled or exceeded.
Estimation of flow duration curve

## Slide 6
The FDC is a key signature of the hydrologic behaviour of a given basin, as it results from the interplay of climatic regime, size, morphology, and permeability of the basin.
From a statistical viewpoint, the FDC is the cumulative probability distribution of the random variable streamflow.
In fact, being the FDC an indication of the frequency with which a given flow is equalled or exceeded, if the observation period is sufficiently long the FDC itself is an approximation of the probability of equalling or exceeding a given river flow.
Note that for a real random variable the probability of "equalling or exceeding" is technically coincident with the probability of "exceeding". Remember that the frequency of an event is an approximation of its probability. We will discuss about probability theory and its implications later on.
Estimation of flow duration curve

## Slide 7
The construction of FDC from a time series of river flows observed at a given and fixed time step is straightforward. One should:
1) Pool all observed streamflows in one sample.
2) Rank the observed streamflows in ascending order.
3) Identify the position of the ith observation in the ordered sample, which coincides with an estimate of the exceedance probability of the observation.
4) Plot each ordered observation versus its position, in relative or absolute terms (i.e., in percentage terms with respect to the observation sample size or actual position; for instance, from 1 to 365 for daily values over an observation period of one year in absolute terms).
Estimation of flow duration curve for a gauged site

## Slide 8
Estimation of flow duration curve for a gauged site - alternative

## Slide 9
Flow regimes based on the FDC

## Slide 10
Estimation of design water withdrawal
Cost-benefit analysis – depends on the water use.
When designing run-of-the-river hydropower plants, it is usual practice to adopt as design flow the river discharge with a duration of 60 days over an observation period of one year, namely, 15-20% of the year. Once the design water withdrawal Qp is fixed, the FDC allows one to estimate the volume of withdrawn water, by also taking into account the release of the environmental flow. The procedure is presented by the graph in Figure 5

## Slide 11
Estimation of design water withdrawal

## Slide 12
Estimation of design water withdrawal
Once Qp is defined, it is possible to compute the average withdrawn river flow Qmp. Then, one can compute the following indexes which quantify the impact of the withdrawal:
- Water withdrawal index Ic=Qp/Qm, where Qm is the average river flow in pristine conditions.
- Water use index Iu=Qmp/Qm.

## Slide 13
Estimation of design water withdrawal

## Slide 14
Inductive assessment of groundwater availability

## Slide 15
Inductive assessment of groundwater availability
Aquifer testing and aquifer monitoring are possible means to inductively understand groundwater dynamics. Testing and monitoring is traditionally carried out through wells. An aquifer test (or pumping test) is carried by constantly pumping water from a selected well and observing the aquifer's response, in terms of changes in the water table elevation, in nearby wells. A rapidly lowering groundwater table, in response to a pumping test, indicates that the aquifer has a slow recharge. Conversely, if nearby wells are not impacted by the pumping test then one may conclude that the aquifer is rapidly recharging.
Groundwater monitoring through wells is carried out by regularly observing the groundwater level in selected wells where significant pumping is applied. In this case as well, a groundwater level that is not significantly impacted by pumping indicates that the aquifer is not negatively affected by water withdrawal.

## Slide 16
Inductive assessment of groundwater availability
Another possibility to infer aquifer dynamic is to estimate water age. If water withdrawn from a well is very old, it means that the aquifer has a slow recharge. The opposite conclusion is reached when it turn out that water is young, though in this case concerns may arise about aquifer vulnerability to contamination, as fast recharge indicates that groundwater flows close to the topographic surface. The age of groundwater ranges from few hours to million years, or perhaps more. Groundwater age can be determined by referring to tracers, including isotopes. For instance, Carbon 14 is frequently used for dating very old water.